Redback Roller Reamer

Assembly Job Card

| BODY SERIAL No. |  |  | TOOL SIZE RANGE |  |
| --- | --- | --- | --- | --- |
| CUTTER SERIAL No. |  |  | CONNECTION SIZE UP |  |
| CUTTER TYPE |  |  | CONNECTION SIZE DOWN |  |
| DATE of ASSEMBLY |  |  | STRING / NEARBIT |  |
| DATE OF CHECK |  |  | 3 POINT / 6 POINT |  |
| DATE of DEPARTURE |  |  |  |  |

| ITEM | DESCRIPTION | Pass/fail | DOC. REF |
| --- | --- | --- | --- |
| 1.0 | Clean pockets with degreaser or solvent cleaner Visually inspect the body and pocket for any mechanical damage Visually inspect the condition of the Helicoil inserts. REPLACE any helicoil that is damaged or protruding above the base of the pocket surface Helicoil Replaced: YES/NO Number Replaced: ………….. Place a New wedge in the cutter pocket to check if any wear is present. Record wear (mm): ……….. |  | MM-SSR-1S Page 9 MM-SRR-1S Page 13 MM-SRR-1S Page 12-13 MM-SRR-1S Page 9 |
| 2.0 | Apply grease or thread compound to complete pocket area |  | MM-SRR-1S Page 9 |
| 3.0 | Lower cutter into pocket and fit wedges |  | MM-SRR-1S Page 10 |
| 4.0 | Wedge Bolts |  | MM-SRR-1S Page 10 |
| 4.1 | Tighten up wedge bolts evenly and torque Tool Range Size Torque Setting 561 Redress Kit 280 ft lbs 514 Redress Kit 280 ft lbs 445 Redress Kit 200 ft lbs 375 Redress Kit 100 ft lbs 350 Redress Kit 80 ft lbs 299 Redress Kit 55 ft lbs TORQUE WRENCH S/N CALIBRATION DUE DATE | Actual Torque | MM-SRR-1S Page 6 |
| 5.0 | Gauging of the Cutters (Gauging to be done over top row of buttons – ensure Correct alignment as per Ref: 2089) Use of appropriate size gauge ring Tolerance to be nominal +1/64 / -0” |  | MM-SRR-1S Page 5 |
| 6.0 | Finishing Operations |  |  |
| 6.1 | Clean and degrease the tool Apply thread compound to connections Install thread protectors Paint the completed assembly (If required) |  |  |
| 6.2 | Mark Tool with the following details: Tool Serial Number (i.e. Body Serial Number GU****) |  |  |

| SIGNED (Tool Dresser) |  |  | SIGNED (Inspector) |  |
| --- | --- | --- | --- | --- |
| PRINT (Tool Dresser) |  |  | PRINT (Inspector) |  |
| DATE |  |  | DATE |  |